## Slide 1
Sreevatsa Anantharamu
Post-doctoral associate (with Prof. Krishnan Mahesh)
Aerospace Engineering & Mechanics
Some applications of parallel computing in fluid mechanics

## Slide 2
State-of-the-art turbulent flow simulations
https://dept.aem.umn.edu/people/faculty/kmahesh/index.html
Propeller crashback:
Verma, Jang & Mahesh, JFM, 2012, 704
Gas turbine combustor:
Mahesh, Constantinescu and Moin, JCP, 2004, 197
Turbulent flow between parallel plates:
Anantharamu and Mahesh, JFM, 2020, 898
No. of processors range from 100 to 0.5 million
For more information on large scale simulation in fluid mechanics, please see Prof. Mahesh’s website
Jet in crossflow:
Iyer and Mahesh, JFM, 2016, 790

## Slide 3
State-of-the-art in turbulent flow simulation
How to simulate these problems and why are parallel algorithms necessary?
Simulate by numerically solving the Navier-Stokes PDE
  Use numerical methods to convert the above PDE to a linear algebra problem
  Solve the linear algebra problem (Ax=b)
    Need iterative/direct solvers (CG/GMRES), preconditioners (Multigrid, ILU)
  For turbulent flows, the resulting linear algebra problem is large
    Speed and memory become issues
Therefore, parallel algorithms are necessary

## Slide 4
Topic of this lecture
A particularly important linear algebra operation is the sparse matrix-vector multiplication
This lecture will focus on parallel algorithms for this operation
Examples where sparse matrix-vector multiplications arise in fluid mechanics:
  While solving the Poisson problem in incompressible flows using iterative methods
    Jacobi’s method: Until convergence, do
    CG, GMRES: Requires the matrix-vector product , where is an Arnoldi vector
  While performing eigenanalysis of fluid flows using methods such as:
    Power iteration: Until convergence, do and normalize
    Arnoldi: Requires the matrix-vector product , where is an Arnoldi vector
  While solving fluid equations with an explicit time integration scheme
    One such case is considered next

## Slide 5
A simple fluid mechanics problem
Consider the simplest fluid mechanics problem that leads to an unstructured sparse matrix-vector multiplication
Transport of dye in a flow
  For e.g., smoke
How to simulate the concentration of smoke, given the velocity of the flow at each point in the domain?
https://www.youtube.com/watch?v=_q6ozALzkF4
Flow over an airplane wing during take off and landing
Flow over an airplane wing during cruise
Flow over a car and a truck

## Slide 6
At , there is no dye inside the geometry. Therefore,
For, the concentration inside the geometry should satisfy the following PDE:
Equations
Inject dye
Dye comes out
Wall
Wall
Arbitrary geometry
Given velocity vector
: Diffusion coefficient
(For simplicity, we will omit the internal walls due to the airfoil/vehicle)

## Slide 7
At , there is no dye inside the computational domain. Therefore,
For, the concentration inside the computational domain should satisfy the following PDE:
Equations
Inject dye
Dye comes out
Wall
Wall
Computational domain
Given velocity vector
: Diffusion coefficient

## Slide 8
Divide the domain into triangles; the set of triangles is called a mesh/grid
19
10
21
13
24
5
12
11
1
16
6
9
22
7
3
23
14
2
4
20
8
17
15
18
Approximate solution
Approximate the average concentration within each triangle of the mesh at discrete time instants using finite volume method and Adam’s Bashforth time integration (details omitted)
; is the approximate average concentration within triangle at time
is the number of triangles (24 in our case), is the separation between the time instants, and is the number of time instants

## Slide 9
At , there is no dye inside the geometry. Therefore,
For, the concentration inside the geometry should satisfy the following PDE:
Equations
Inject dye
Dye comes out
Wall
Wall
Arbitrary geometry
Given velocity vector
: Diffusion coefficient
(For simplicity, we will omit the internal walls due to the airfoil/vehicle)

## Slide 10
Can write this as a sparse matrix-vector multiplication problem:
  Given and , compute as
  , where is the sparse matrix
  What is the maximum number of non-zeros in any row of A?
Unstructured sparse matrix-vector multiplication problem
The resulting equation for each turn out to be where is a linear combination of some vectors. For e.g., if , then the summation is over
Mesh
Sparsity pattern of A

## Slide 11
Parallel sparse matrix-vector multiplication
Illustrate parallel algorithms for sparse-matrix vector multiplication using this model problem, i.e., given , compute
Simplest algorithm: Two-processor, blocking algorithm
Step #1: Divide rows of matrix A, vectors and between the two processors
  For this lecture, we will use the following simplest strategy to divide the rows
  Assume first 12 rows are stored in rank 0 and remaining 12 rows are stored in rank 1
=
rank 0
rank 1

## Slide 12
Parallel sparse matrix-vector multiplication
Each processor stores only a portion of vector
Therefore, the processors cannot independently evaluate their portion of vector
For e.g., consider row 1 in rank 0:
  and are stored in rank 0, but is stored in rank 1
Therefore, rank 1 needs to send to rank 0 and rank 0 needs to receive from rank 1
Similarly, rank 1 will need to receive some from rank 0 and rank 0 needs to send these to rank 1
=
rank 0
rank 1

## Slide 13
Parallel sparse matrix-vector multiplication
Step #2: Figure out this meta data required for inter-processor communication
Divide the portion of matrix stored within each processor into two portions:
  Portion whose contribution to vector b can be computed just from the portion of stored in the same processor (grey box)
  Portion whose contribution to vector b cannot be computed just from the portion of stored in the same processor (red box)
=
rank 0
rank 1

## Slide 14
Parallel sparse matrix-vector multiplication
Identify the non-zero columns in the red portion within each rank
For rank 0, this is the set
For rank 1, this is the set
This yields the following metadata for our inter-processor communication:
Rank 0 must receive from rank 1, and send to rank 1
Rank 1 must receive from rank 0, and send to rank 0
=
rank 0
rank 1

## Slide 15
Parallel sparse matrix-vector multiplication
Step #3: Allocate space to receive these s from the other processor
Extend the vector within each processor to store this received data
rank 0
Portion stored in rank 0
Space to receive s from rank 1
rank 1
Portion stored in rank 1
Space to receive s from rank 0

## Slide 16
Parallel sparse matrix-vector multiplication
Step #4: Perform inter-processor communication
We will use the simplest MPI point-to-point communication routines MPI_SEND and MPI_RECV
These are blocking communication routines
Blocking means that the program will not proceed further until the communication is finished

## Slide 17
Parallel sparse matrix-vector multiplication
Blocking MPI communication
Matrix-vector multiplication
Code snippet (Fortran)
I will give the full code to Chris, and he will distribute it to you!

## Slide 18
Parallel sparse matrix-vector multiplication
Improvisation #1: Two processors, non-blocking
Blocking communication is not optimal because the program stagnates until the communication is finished
Can overlap computation and communication
This will mask the time spent in communication
For e.g., again consider row 1 in rank 0:
Can compute the partial sum from the first three terms (highlighted in grey) while receiving from rank 1
Use non-blocking MPI point-to-point communication routines MPI_ISEND and MPI_IRECV

## Slide 19
Initiate non-blocking MPI communication
Code snippet
Compute partial sum from s stored within the processor
Finish communication
Append the partial sum from the s received and to the previous partial sum

## Slide 20
Parallel sparse matrix-vector multiplication
Improvisation #2: Large number of processors and rows, blocking/non-blocking
Say, 1 billion rows and 0.1 million processors!
The algorithms discussed won’t work
Two major issues:
  Linear decomposition of rows may not be optimal
    By optimal, we mean least amount of data exchanged between processors
    Need graph partitioning
    Libraries: METIS, ParMETIS, Zoltan, SCOTCH, Mongoose
  Need a scalable algorithm to ascertain the metadata necessary for inter-processor communication
    Complicated, but possible!
1.3 billion rows divided into 0.14 million processors using ParMETIS

## Slide 21
Supercomputers used by our research group
Supercomputer | Number of processors
Mira (ANL) | 0.78 million
Stampede2 (XSEDE) | 0.29 million
Narwhal (DOE) | 0.29 million
Onyx (DOE) | 0.12 million
Centennial (DOE) | 72 thousand
Mustang (DOE) | 56 thousand
Mangi (MSI) | 20 thousand
Mesabi (MSI) | 18 thousand
Horne and Mahesh, JCP, 2019, 376
An example large-scale computation within our group
If you are interested, please contact Prof. Mahesh
kmahesh@umn.edu